## Slide 1
Constraining Global Estimates of Aerosol Direct Radiative Forcing and Surface Concentrations
Glory Science Team
08/12/2011
Daven K. Henze, Brian Meland, University of Colorado Boulder
Jun Wang, Xiaoguang Xu, University of Nebraska Lincoln
Drew Shindell, NASA GISS
Robert Spurr, RT Solutions
Monika Kopacz, Kumaresh Singh, Changsub Shim
G
c
adj

## Slide 2: Short Lived Climate Forcing Agents
Aerosol DRF: large and uncertain
AR4, Forster et al.,
2007

## Slide 3: Systems for modeling air quality & climate change

## Slide 4: Refining the RF bar chart
Sector specific contributions: Fuglestvedt et al., 2008
Unger et al., 2008
Sector and regional specific contributions: Unger et al., 2008

## Slide 5: Systems for modeling air quality & climate change
Calculating DRF becomes computationally intractable...

## Slide 6: Radiative Forcing Transfer Functions
How to calculate the radiative forcing change for
a given change in emissions?
Using transfer function T:

## Slide 7: Radiative Forcing Transfer Functions
How to calculate the radiative forcing change for
a given change in emissions?
Using transfer function T:
Approximate T using adjoint:

## Slide 8: Radiative Forcing with GEOS-Chem
Radiative Transfer Code
Mie Code
linearized
GC Adj
Weighting functions
Henze et al.,
2007
GEOS-Chem
Mie Code
[SIA], [BC], [OC], Ddry
Radiative Transfer Code
LIDORT (Spurr, 2002)
TOA upward SW flux
Forward model
Sensitivity calculation:

## Slide 9: Aerosols and Radiative Forcing
Sensitivities from every sector and region:
Calculated very efficiently using GEOS-Chem adjoint
(Henze et al., 2007) and LIDORT (Spurr, 2002)

## Slide 10: Direct Radiative Forcing efficiencies
The % change in radiative forcing per change in emission:
Variability indicates importance of hi-res analysis
Emissions of BC
Emissions of NH3
W m-2 / (kg m-2 yr-1)

## Slide 11: Validation
Notes: \frac{\partial \mbox{[NO}_3^{--}]}{\partial {E}_{\mbox {NH}_3}}
\frac{\partial RF}{\partial {E}_{\mbox {SO}_2}}
\frac{\partial RF}{\partial {E}_{\mbox {BC}}}

## Slide 12: Validation: lumped impacts
perturb x 100% | Adjoint esitimate [W/m2] | Forward model RF [W/m2]
OC | -0.10 | -0.13
BC | 0.23 | 0.21
SO2 | -0.27 | -0.27
NH3 | -0.07 | -0.06
NOx+NH3+SO2 | -0.72 | -0.86

## Slide 13: Apply to RCP45 2050 scenario

## Slide 14: Apply to RCP45 2050 scenario

## Slide 15: Efficiency vs magnitude of emissions
Consider the cell-by-cell relationship:

## Slide 16: Efficiency vs magnitude of emissions
aggregated by sector:

## Slide 17: Ok, but what is Gloryous about this?
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool
1. Species / Sectors / Regions with large heterogeneity in efficiency and large uncertainty in emissions play large role in DRF.
Improving estimates of aerosol sources and distributions will lead to enhanced utility of DRF.
Observations from APS / RSP and additional platforms can help us constrain these factors.

## Slide 18: What role does polarimetry play?
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool
Have considered constraints on aerosol properties and aerosol classification.
To what extent could APS observations provide constraints on aerosol composition vs model parameters?
To what extent can these constraints be propogated back through a model to constraints on sources?

## Slide 19: Sensitivity of polarization with respect to layer-by-layer aerosol properties using VLIDORT+linearized MIE
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool
w.r.t. mean radius
w.r.t. refractive index
• relate to emissions
• test more conditions
• explore more multi-
facted metrics
• develop rankings
Brian Meland, CU Boulder

## Slide 20: In practice: regional scale assimilation
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool
Have begun with MODIS:
Will continue with RSP+
optimized SO2 emission
a priori SO2 emission
Xiaoguang Xu, UNL

## Slide 21: Final remarks
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool
Adjoint sensitivities can provide high-resolution estimates of aerosol DRF
The same tools can be used to rank optically based metrics in terms of constraint potential
The same tools can be used for assimilation of remote sensing products in a cyclic process of improving model estimates of radiative forcing

## Slide 22: the end
Focus on radiative forcing rather than effects:
- how much of the influence comes from
anthropogenic emissions?
- what is the RF for different emissions scenarios?
--> potential as screening tool